## Slide 1
Under Supervisors:
Dr. Ahmed Ayoup Dr. Haitham
DIGITAL CLOCK
Logic design

## Slide 2
01
1) Idea, motivation and Problem State, Merits of the project.
04
4) Code and simulation of project .
02
2) Part list and Schematic of project.
05
5) Future work and Appendix
03
3) Mechanical Parts.
Outline

## Slide 3
The main idea of this project is to build a simple digital clock using an Arduino. The clock will show the current time using a display, and it will keep track of time accurately with the help of a Real-Time Clock (RTC) module.
The motivation for this project comes from the goal of applying logical design concepts to something practical and useful. Digital clocks are devices we see every day, and creating one helps us understand how time is measured, stored, and shown using digital systems.
Project Vision and Motivation

## Slide 4
1
2
3
  Old Code: 12-hour format with AM/PM toggle.
  New Code: 24-hour format (goes from 0 to 23).
Time Format:
  Old Code: Buttons for adjusting hours, minutes, and toggling AM/PM.
  New Code: Buttons for adjusting hours, minutes, and resetting seconds. No AM/PM toggle.
Button Handling:
Problem statement of project
  Old Code: Seconds, minutes, and hours reset as needed.
  New Code: Only resets seconds (doesn't reset hours or minutes).
Full Reset:

## Slide 5
Future work and Improvement
1.Problems with Logic Gates
At first, we had trouble setting up the logic gates correctly. It took us time to understand how to make the right connections and get the expected results.
3. Pushbutton Confusion
We started with 2-pin pushbuttons, which were hard to wire correctly. Later, we switched to 4-pin buttons, which were easier to connect and gave better results.
2. Components Burning in Tinkercad
While testing the circuit on Tinkercad, some parts kept "burning" or not working properly. This was usually because of wrong connections or voltage issues, and we had to fix the wiring many times.
4 . Using a Regular LCD Instead of I2C
We chose a normal 16x2 LCD instead of an I2C one to have more control over the display. But this meant using more wires and Arduino pins, which made the setup harder to manage.

## Slide 6
Parts list and Schematic of project
•Arduino Uno
• R3LCD 16 x 2
•1 kΩ Resistor (×4)
•220 Ω Resistor (×1)
•Pushbutton (×3)
•Inverting Schmitt Trigger (74HC14)
Buzzer (Passive or Active)

## Slide 7
Mechanical Parts
•Arduino Uno
• R3LCD 16 x 2
•1 kΩ Resistor (×4)
•220 Ω Resistor (×1)
•Pushbutton (×3)
•Inverting Schmitt Trigger (74HC14)
Buzzer (Passive or Active)

## Slide 8
#include <LiquidCrystal.h>
#include <EEPROM.h>
// LCD Pins
LiquidCrystal lcd(2, 3, 4, 5, 6, 7);
// Button Pins
#define MODE_BUTTON 8
#define INC_BUTTON 9
#define DEC_BUTTON 10
#define ALARM_TOGGLE 11
#define BUZZER_PIN 12
// Variables
int hours, minutes, seconds;
bool isPM;
int alarmHours = 7, alarmMinutes = 0;
bool alarmIsPM = false;
bool alarmEnabled = false;
bool alarmTriggered = false;
Code
int adjustMode = 0;
// 0=Normal, 1=Hour, 2=Minute, 3=AM/PM, 4=Alarm Hour, 5=Alarm Minute, 6=Alarm AM/PM
//Date and Day
const char* currentDate = "29/04/2025";
const char* currentDay = "Tue"
// Timing
unsigned long lastUpdate = 0;
unsigned long lastButtonPress = 0;
const unsigned long debounceDelay = 100;
unsigned long snoozeUntil = 0;

## Slide 9
void setup() {
lcd.begin(16, 2);
pinMode(MODE_BUTTON, INPUT_PULLUP);
pinMode(INC_BUTTON, INPUT_PULLUP);
pinMode(DEC_BUTTON, INPUT_PULLUP);
pinMode(ALARM_TOGGLE, INPUT_PULLUP);
pinMode(BUZZER_PIN, OUTPUT);
hours = EEPROM.read(0);
minutes = EEPROM.read(1);
seconds = EEPROM.read(2);
isPM = EEPROM.read(3);
updateDisplay();
}
void loop() {
unsigned long now = millis();
Code
if (now - lastUpdate >= 800)
lastUpdate = now;
updateTime();
checkAlarm();
updateDisplay();
}
handleButtons();
}
void handleButtons() {
if (millis() - lastButtonPress < debounceDelay) return;

## Slide 10
Code
if (digitalRead(MODE_BUTTON) == LOW) {
adjustMode = (adjustMode + 1) % 7;
updateDisplay();
lastButtonPress = millis();
}
if (digitalRead(ALARM_TOGGLE) == LOW) {
if (alarmTriggered) {
snoozeUntil = millis() + 5UL * 60UL * 1000UL;
alarmTriggered = false;
noTone(BUZZER_PIN);
} else {
alarmEnabled = !alarmEnabled;
}
updateDisplay();
lastButtonPress = millis();
}
if (digitalRead(INC_BUTTON) == LOW && adjustMode > 0) {
adjustValue(1);
updateDisplay();
lastButtonPress = millis();
}
if (digitalRead(DEC_BUTTON) == LOW && adjustMode > 0) {
adjustValue(-1);
updateDisplay();
lastButtonPress = millis();
}
}

## Slide 11
Code
void updateTime() {
seconds++;
if (seconds >= 60) {
seconds = 0;
minutes++;
if (minutes >= 60) {
minutes = 0;
hours++;
if (hours > 12) {
hours = 1;
isPM = !isPM;
}
}
}
EEPROM.write(0, hours);
EEPROM.write(1, minutes);
EEPROM.write(2, seconds);
EEPROM.write(3, isPM ? 1 : 0);
}
void checkAlarm() {
if (alarmEnabled && !alarmTriggered && millis() > snoozeUntil) {
alarmTriggered = true;
}
}
if (alarmTriggered) {
digitalWrite(BUZZER_PIN, HIGH);
lcd.display();
} else {
digitalWrite(BUZZER_PIN, LOW);
lcd.display();
}
}

## Slide 12
Code
void adjustValue(int change) {
switch (adjustMode) {
case 1:
hours += change;
if (hours > 12) hours = 1;
if (hours < 1) hours = 12;
break;
case 2:
minutes += change;
if (minutes >= 60) minutes = 0;
if (minutes < 0) minutes = 59;
seconds = 0;
break;
case 3:
isPM = !isPM;
break;
case 4:
alarmHours += change;
if (alarmHours > 12) alarmHours = 1;
if (alarmHours < 1) alarmHours = 12;
break;
case 5:
alarmMinutes += change;
if (alarmMinutes >= 60) alarmMinutes = 0;
if (alarmMinutes < 0) alarmMinutes = 59;
break;
case 6:
alarmIsPM = !alarmIsPM;
break;
}
}
void updateDisplay() {
lcd.clear();
lcd.setCursor(0, 0);
if (hours < 10) lcd.print("0");
lcd.print(hours);
lcd.print(":");
if (minutes < 10) lcd.print("0");
lcd.print(minutes);
lcd.print(":");
if (seconds < 10) lcd.print("0");
lcd.print(seconds);
lcd.print(isPM ? " PM" : " AM");

## Slide 13
Code
lcd.setCursor(0, 1);
lcd.print(currentDay);
lcd.print(" ");
lcd.print(currentDate);
if (alarmEnabled) {
lcd.setCursor(10, 1);
lcd.print("ALM");
lcd.print(" ");
if (alarmHours < 10) lcd.print("0");
lcd.print(alarmHours);
lcd.print(":");
if (alarmMinutes < 10) lcd.print("0");
lcd.print(alarmMinutes);
lcd.print(alarmIsPM ? "PM" : "AM");
}
if (adjustMode > 0) {
lcd.setCursor(0, 1);
switch (adjustMode) {
case 1:
lcd.print("Set Hour [+][-]");
break;
case 2:
lcd.print("Set Min [+][-]");
break;
case 3:
lcd.print("Set AM/PM [+]");
break;
case 4:
lcd.print("Alm Hour [+][-]");
break;
case 5:
lcd.print("Alm Min [+][-]");
break;
case 6:
lcd.print("Alm AM/PM [+]");
break;
default:
lcd.print("Time Mode");
break;
}
}
}

## Slide 14
Team Names
1. Mariam Abdallah Mohamed _692400624 _E1
2. Malak Emad Abdelnabie_ 692400649 _E1
3. Nourhan Hamed Serageldin _692400663 _E1
4. Abdallah Emad Ragab 692400175 D1
5. Mohamed Osama Ahamed _692400638_E1
6. Ahmed Waled Shawky_622400006_B3
7. Mohamed Tarek Abdelaziz _692400158_C5
8. Gamal Sayed Mohamed _692400633_G1
9. Begad Sameh Salah_692400620_E1
10. Ziad Emad _692400574 _D4
11. Yasmine Yasser Motawe _ 692400099_A5
12. Mohamed Ayman Ahmed_692400560_D2
13. Mohamed Mahmoud Mohamed_692400363_C3
14. Ahmed Samy Mohamed_ 692400458_ E1
15. Youssef Ahmed Mostafa Hawary_692400157_D1
16. Mohamed Faisal Mohamed _692400112_D3
17. Nancy Hussein Morsy_692400618_A3
18. Seif Eldeen Ahmed_692400509 _E1
19 .Yassin Amr Mohamed_692400629_E2
20. Hossam Mohamed_692400581_B5

## Slide 15
  LCD 16x2 display connected to digital pins on the Arduino Uno
  Pushbuttons connected to digital inputs, with pull-down resistors (1kΩ)
  220Ω resistor used for the buzzer or as a current limiter for an LED if included
  Schmitt Trigger (74HC14) used for debouncing button inputs or signal conditioning
  Buzzer (active or passive) for alarm or timer notification
  The Schmitt Trigger (74HC14) ensures clean, noise-free button presses by shaping input signals.
  Pushbuttons can be programmed to adjust the clock settings (e.g., set hour, minute, reset).
  The buzzer can be used for a basic alarm or to confirm time-setting actions.
  The LCD displays the time clearly and updates continuously in the loop()
The appendix

## Slide 16
TA Esraa,
Thank you so much for helping us with the project! Your support made a difference, and we’re grateful for your time and effort. It made things a lot easier and less stressful.
Thanks again for everything!

## Slide 17
Thank
You